File ID: TIRE009

_____________________________________________________________

IMPLEMENTATION OF LOCAL COMPETITION

CRTC INTERCONNECTION STEERING COMMITTEE

REPORT to the CRTC

by

INDUSTRY SUB-GROUP

Technical Interface

TIF 3 Minimum CCS7 Message Set

Consensus Report

________________________________________________________________

TITLE: Minimum CCS7 Message Set pursuant to Telecom Order 98-40

________________________________________________________________

DATE:	March 3, 1998

________________________________________________________________

Every LEC operating under Decision 97-8 must exchange the message necessary to support the following base capabilities:

Basic CCS7 Call Control

Calling Line Identification Presentation & Restriction Services

Call Forwarding Services

The TISWG agreed that based on services currently offered, the CCS7 messages to be supported associated with the “multi-laterally supported services” pursuant to Telecom Order 98-40 include:

Select CMS and Custom Calling Features (See TISWG spec).

ISDN (largely NI-1 features, TR444 based).

Toll-free carrier selection (TISWG discussed).

Calling Name.

Messages associated with mandated interworking:

LNP

As noted in item “i” of the "multi-laterally supported services", the TISWG has developed the interface specification Call Management Features which includes the information required for the following features:

Automatic Callback (AC)
An outgoing call management feature that enables a customer encountering a busy station to perform an activation procedure and have call setup performed automatically when the called station becomes idle.

Automatic Recall (AR)
An incoming call management feature that enables a customer to perform an activation procedure and automatically redial the last incoming number without having to know the number or even who the calling party was.

Screening List Editing
A network capability allowing a subscriber to maintain a list of telephone numbers that will be used by other call management services. For example, a local carrier network could provide a feature that allows a subscriber to receive a distinctive ringing signal when receiving a call from a telephone number on a screening list.

It should also be noted that the TISWG agreed that there is a requirement to develop interface specifications to support the ISDN associated messages.

# Footnotes

Network–to–Network Technical Interface for Local Interconnection Call Management Features, version 0.3, April 9, 1997